Gaslighter V1 Engine
FINAL REVIEW
Gaslighter V1 Engine
FINAL REVIEW
Designer: Karl Kanmaz
Systems Engineer: Joe Wilson

---
GL V1 Ideal System Specs
GL V1 Ideal System Specs
- Chamber Pressure = 150 psi
- Throat Diameter = 1.33 in
- Bulk Chamber Temp = 1937 F
- L* = 30 in
- MR = 1.06
- Area Ratio = 2.25
- Mass flow = 1.68 lbm/s
Max Thrust = 267.2 lbs

---
Propellant
- Fuel = 99% Ipa
- Oxidizer = N2O (Automotive)
- Combustion properties from CEA

---
Engine
- Chamber pressure chosen to keep fuel runtank < 200psia
- Engine mdot limited by fuel runtank pressures and volume (0.5gal/5s)
- Mixture ratio chosen to keep chamber temps 10% over melting (1730F)
- Atmospheric Pressure = 14.66psia (Mojave Barametric @100F)

---
Propellant Tanks
Tank was chosen purley on cost and for lack of fabrication, for higher chamber pressures tapping the bottom of the nitrogen bottle and buying a 3/4” UNF fitting and proofing the assembly per B31.3 would be very cost effective

---
Ambient Properties
Frontiers of Solidifcation (MPMD 2016)
Heat Sink Modeling
- Assumes 100% Combustion Efficiency
- Throat temp = Chamber temperature
- Diffusivity chosen based on median flame temp (293K -> 1250K)
- Copper C360 (Brass) chosen to balance cost, melting temp and conductivity
- Heat transfer done with FDM discrete and rk4 integration
Ambient Diffusivity (293K) = ~3.59e-5 [m2/s]
Frontier Model Diffusivity(293K) = ~3.51e-5 [m2/s]
Frontier Model Diffusivity(771K) = ~3.89e-5 [m2/s]
Calc is likely conservative, but this demonstrates worst case conditions, and drives starting mixture ratio selection.
Melting temp 1160K
(0.141in)!
1244K [FROM CEA]
780K
Adiabatic Outer Wall Temp

---
What happens as the throat errodes?
  - Major performanc reductions form Thrust, Cstar and Exit Velocity losses
  - Expansion ratio is reduced, leading to underexpansion and much higher nozzel exit pressures
  - Chambers temps go down slightly (~20K) <- at extremes this actually leads to chamber temps less than melting
Throat Errosion
231lbf
(6% Reduction)
121psia Chamber Pressure (20% Reduction)
Even with max expected errosion during a 5s burn, thrust loss is minimal
for this reason, throat errosion with brass was taken as acceptable

---
Design
Design
Chamber
Material: 6061 T6 Tube
Adjustable
Injector
Material: 6061 Aluminum
Clamp Plate
Material: Mild Steel
Graphite Gasket
Throat-Nozzle
Material: 360 Brass

---
Pressure Ladder
Mdot_fuel = 0.65 lbm/s (0.29 kg/s)
V_tank = 0.011 m^3
Ullage % = 10%
Mass_fuel_max = 8 kg
Max Burn Time = 28 s
Pressure Ladder
Branch Pipe 2X
Dp = 2.2 psi
P = 182.1 psi
Length = 10”
⌀ 0.375”
Roughness = …
Injector Orifice 2X
Dp = 31.3 psi
P = 150 psi
⌀ 0.155”
Sump
Outlet Pipe
Dp = 2.6 psi
P = 184.3 psi
Length = 4.9 ft
⌀ 0.44”
Relative Roughness= 0.0015
Ball Valve - 052
Dp = 0.2 psi
P = 186.8 psi
Cv = 11.7
Sump
Dp = 0
P = 187 psi
⌀ 0.5”
Cd = 0.65
Fuel Tank
187 psi
F-V-052
Injector
Chamber
150 psi

---
Load - Cell Threads
Load - Cell Threads
2X ¼” - 28 Thread
Length = 0.5”
Athread = PI*dm*Le / 3
Fsu = 30 ksi
FOS = 2
Pallowed = 2000 lbf (per thread)
Aluminum threads may wear after many uses, be prepared to insert helicoil replacement

---
Chamber Pressure Stress
Chamber Pressure Stress
Hoop Stress = Pr/t
= (150 psi) * (1.75”) / (0.25”)
= 1050 psi [7 MPa]
- FOS_ult = 2
- Temp should be limited to approx. 400 Celsius ( 752 F)