Gaslighter V1 Engine
FINAL REVIEW
Gaslighter V1 Engine
FINAL REVIEW
Karl Kanmaz, Joe Wilson

---
Engine
- Chamber pressure chosen to keep fuel runtank < 200psia
- Engine mdot limited by fuel runtank pressures and volume (0.5gal/5s)
- Mixture ratio chosen to keep chamber temps 10% over melting (1730F)
  - This is an conservative choise, based on combustion efficency expectations
Design decisions on this
motor are intended to provide
an easy onramp to liquid propolsion
instead of optimizing performance.

---
Propellant
- Fuel: 99% Ipa
- Oxidizer: N2O (Automotive)
- Combustion properties from CEA
Propellants chosen for their ease of use and avaliblity, at the cost of performance.
Additional complexity is added by the use of a high vapor pressure oxidizer, this was perfered over the challanges of cryogenics for a small hobby project.

---
GL V1 Ideal System Specs
GL V1 Ideal System Specs
- Chamber Pressure = 150 psi
- Throat Diameter = 1.33 in
- Bulk Chamber Temp = 1937 F
- L* = 30 in
- MR = 1.06
- Area Ratio = 2.25
- Mass flow = 1.68 lbm/s
Max Thrust = 267.2 lbs

---
Design
Design
Chamber
Material: 6061 T6 Tube
Adjustable
Injector
Material: 6061 Aluminum
Clamp Plate
Material: Mild Steel
Graphite Gasket
Throat-Nozzle
Material: 360 Brass

---
Ambient Properties
Heat Sink Modeling
Frontiers of Solidifcation (MPMD 2016)
- Assumes 100% Combustion Efficiency, and perfectly caloric products
- Throat temp = Chamber stagnation temperature
- Diffusivity chosen based by median flame temp (293K -> 1250K)
- Copper C360 (Brass) chosen to balance cost, melting temp and conductivity
- Heat transfer done with FDM discrete and rk4 integration
Ambient Diffusivity (293K) = ~3.59e-5 [m2/s]
Frontier Model Diffusivity(293K) = ~3.51e-5 [m2/s]
Frontier Model Diffusivity(771K) = ~3.89e-5 [m2/s]
Calc is likely conservative, but this demonstrates worst case conditions, and drives starting mixture ratio selection.
Melting temp 1160K
(0.141in)!
1244K [FROM CEA]
780K
Adiabatic Outer Wall Temp

---
Throat Errosion
Based on conservative heat sink modeling, throat erosion is likely.
Effects of this:
  - Chamber pressure reduction
  - Exit Ratio decreases inverse with Exit Pressure and proportional to Exit velocity
  - Slight Chamber temperature reduction
  - Increased mdot from both injectors
  - For small erosion thrust increases, until exit velocity compromises mdot increase
Risks:
  - Reduced injector stiffness (instability, or combustion gas up the feedline)
  - Loss of engine performance
    (lower isp, transition to under expansion and decreased exit velocity)
Thrust
Expansion = Unity
Even with max expected errosion during a 5s burn, thrust loss is minimal.
Injector stiffness risk will be accepted, and mitigated with an intial lower duration burn to access erosion

---
Load - Cell Threads
Load - Cell Threads
2X ¼” - 28 Thread
Length = 0.5”
Athread = PI*dm*Le / 3
Fsu = 30 ksi
FOS = 2
Pallowed = 2000 lbf (per thread)
Aluminum threads may wear after many uses, be prepared to insert helicoil replacement

---
Chamber Pressure Stress
Chamber Pressure Stress
Hoop Stress = Pr/t
= (150 psi) * (1.75”) / (0.25”)
= 1050 psi [7 MPa]
- FOS_ult = 2
- Temp should be limited to approx. 400 Celsius ( 752 F)

---
Test P&ID / Instrumentation
Risk Profile:
  - 2 Fault tolerant during manual operations
  - 1 Fault tolerant to loss of GSE
  - 0 Fault tolerant to engine loss
Nitrous:
  - Nitrous outlet 20lbm + high flow siphon valve
  - Pressure / Temp at all major locations
  - Redundant purge checks to mitigate leakage flowing
    into fuel system if checked off
  - 4 x calibrated load cells to measure mass usage against injector mdot
IPA:
  - IPA temperature considered ideally constant, only ullage pressure
    and injector fluid state are measured
  - 4 x calibrated load cells to measure mass usage against injector mdot
Purge:
  - Limits moisture (from icing in Nos leakage or combustion products)
  - Acts as a small gas damper during startup (startup timing tbd)
Chamber:
  - Chamber pt with thermal standoff
  - Chamber temperatures although low enough to measure with a K-type TC where not installed
    due to possibilities of increased chamber temps in the future
  - 3 x Skin temperature sensors on injector wall, chamber wall and throat location
If budget allowed normally open valves , a remote pressurant isolation, and a separate volume
for purge gas would have been desirable from a test stand perspective.

---
Mdot_fuel = 0.65 lbm/s (0.29 kg/s)
V_tank = 0.011 m^3
Ullage % = 10%
Mass_fuel_max = 8 kg
Max Burn Time = 28 s
Pressure Ladder
Branch Pipe 2X
Dp = 2.2 psi
P = 182.1 psi
Length = 10”
⌀ 0.375”
Roughness = …
Injector Orifice 2X
Dp = 31.3 psi
P = 150 psi
⌀ 0.155”
Sump
Outlet Pipe
Dp = 2.6 psi
P = 184.3 psi
Length = 4.9 ft
⌀ 0.44”
Relative Roughness= 0.0015
Needle Valve - 052
Dp = 0.2 psi
P = 186.8 psi
Cv = 11.7
Sump
Dp = 0
P = 187 psi
⌀ 0.5”
Cd = 0.65
Fuel Tank
187 psi
F-V-052
Injector
Chamber
150 psi

---
Purge Sizing
- Control Mass Flow by choking upstream of feedlines this ensures down stream conditions do not effect purge mass flow-rate until critical conditions are met
- Ensure a minimum of 3 x volume exchanges based onNASA Lessons Learned (For hydrogen but few sources exist for nitrous oxide / IPA)

---
Fuel Tank
Fuel Tank was chosen purley on cost and for lack of fabrication, for higher chamber pressures tapping the bottom of the nitrogen bottle, buying a 3/4” UNF fitting and proofing the assembly per B31.3 would be very cost effective

---
DESIGN